## Slide 1
Aeolus: A Building Block for
Proactive Transport in Datacenters
Shuihai Hu (Clustar&HKUST), Wei Bai (Microsoft&HKUST), Gaoxiong Zeng,
Zilong Wang, Baochen Qiao, Kai Chen, Kun Tan (Huawei), Yi Wang (PCL)
SING Lab @ Hong Kong University of Science and Technology
Notes: Hello everyone, I am Shuihai Hu from Clustar and HKUST. Today, I would like to talk about our work Aeolus, which proposes a new building block to augment proactive transports. [click]

## Slide 2: Era of High-speed DCNs
The link speed of production DCNs grows fast:
1Gbps
2007
10Gbps
2010
40Gbps
2013
100Gbps
2016
2020
200Gbps
…
Notes: In recent years, as shown in the figure, the link speed of production DCNs grow very fast, from 1Gbps to 10Gbps, to 100Gbps with 200Gbps on the horizons.[click]

## Slide 3: Congestion Control Becomes More Challenging
10-100X link speed
10-100x higher BDP (bandwidth-delay product)
More bustiness
Flows finish in much fewer RTTs
Notes: Given this trend, congestion control in DCNs have become more challenging. [c] With link speed increased by 10-100 times, [c] today’s DCNs have much higher bandwidth-delay product and more bustiness. [c] and flows now finish in much fewer RTT, leaving the transport very little time to react to congestion. [c]

## Slide 4: Congestion Control Today
Current solution: mainly using reactive protocols
  TCP, DCTCP, TIMELY, …
  react to signals after congestion occurs
Large switch queues
Severe loss under incast
Very slow convergence
Worse with higher link speed
Notes: Today’s congestion control are mainly achieved using reactive protocols. [click] Reactive congestion control algorithms, such as TCP and DCTCP, react only after congestion already happens. [click] Reactive solutions have long-standing problems including switch queue build-ups, severe loss under incast and very slow convergence speed. [click] With higher link speed, all these problems now become worse. [click]

## Slide 5: Proactive Congestion Control (PCC)
Large switch queues
Severe packet loss
Very slow convergence
Reactive Solutions
Near-zero queueing
Zero packet loss
Fast convergence
Proactive Solutions
VS
Notes: proactive congestion control solutions, or PCC, have drawn great attention in recent years. [c] Compared with reactive solutions, proactive solutions have several advantages, including [click] near-zero queueing, [click] zero packet loss, [click] and fast convergence. [click]

## Slide 6: Existing PCC Solutions
Key idea: proactively schedule network transfer using credit
FastPass (Sigcomm’14)
A central arbiter to globally schedule network transfer.
Centralized
Switch Based
PDQ (Sigcomm’12)
TFC (Eurosys’16)
Switches explicitly allocate link bandwidth to flows.
Receiver Based
ExpressPass (Sigcomm’17)
NDP (Sigcomm’17)
Homa (Sigcomm’18)
Receivers explicitly schedule the transfer of packets for different receivers.
Notes: Unlike reactive solutions, the key idea of PCC is to proactively schedule network transfer based on the availability of network resources using credit. The idea of PCC can be realized in several ways. [click] For example, Fastpass employs a centralized arbiter to enforce a tight control over network transfer. [click] PDQ and TFC leverage switches to explicitly allocate link bandwidth among the passing flows. [click] ExpressPass, NDP and Homa use receiver-driven credit-based approaches to explicitly schedule the arrival of data packets destined for different receivers. [c]

## Slide 7: Existing PCC Solutions
Key idea: proactively schedule network transfer using credit
FastPass (Sigcomm’14)
A central arbiter to globally schedule network transfer.
Centralized
Switch Based
PDQ (Sigcomm’12)
TFC (Eurosys’16)
Switches explicitly allocate link bandwidth to flows.
Receiver Based
ExpressPass (Sigcomm’17)
NDP (Sigcomm’17)
Homa (Sigcomm’18)
Receivers explicitly schedule the transfer of packets for different receivers.
One extra RTT is required to prepare the schedule!
Notes: While being promising, all existing PCC solutions require one extra RTT to prepare the schedule. In high speed networks, we find that, the cost of delaying all flows by one extra RTT can be very expensive.[c]

## Slide 8: The first RTT Matters!
Observation: At high link speed, a large portion of flows could finish in the 1st RTT
At 100Gbps, 60%-80% of flows could have been finished within the first RTT!
Notes: [c] Our observation is that, at high link speed, a large portion of flows could complete in the first RTT. [c] In this figure, we show the fraction of flows could have been finished within the first RTT under different link speeds. Although our measurement methodology is idealized, the results suggests a clear trend that the rise of high-speed DCNs makes the first RTT much more important. [c] As we can see, At 100Gbps, 60-80% of flows could have been finished within the first RTT! [c]

## Slide 9: Current Practice for Handling the One Extra RTT
#1: Pay the cost of one extra RTT
Credit Request
Sender
Receiver
ExpressPass needs one RTT to prepare data transmission
Notes: However, existing solutions cannot well handle the one-extra-RTT problem. They mainly fall in two categories. [click] One line of work choose to pay the cost of one extra RTT. [c] For example, in ExpressPass, [c] the sender will send a credit request to the receiver on the arrival of a new flow. [c]

## Slide 10: Current Practice for Handling the One Extra RTT
#1: Pay the cost of one extra RTT
Credit
2nd rtt:
data
Sender
Receiver
ExpressPass needs one RTT to prepare data transmission
Notes: [c] On receiving credit request, the receiver will send credits to the sender. [c] The sender will send data packets after it receives credit. So all flows are delayed by at least one RTT. [c]

## Slide 11: Current Practice for Handling the One Extra RTT
80% of Small flows take one extra RTT to complete
#1: Pay the cost of one extra RTT
FCTs of 0-100KB flows with 100Gbps link speed
one extra RTT
Notes: At high speed, the cost of wasting 1st RTT can be very expensive! [c] To demonstrate this, we measure the FCT of 0-100KB small flows with 100Gbps link speed. Flows are generated according to Cache Follower workload. [c] As we can see, compare with idealized solution, 80% of Small flows take one extra RTT to complete when under ExpressPass. [c]

## Slide 12: Current Practice for Handling the One Extra RTT
#1: Pay the cost of one extra RTT
#2: Blindly burst traffic in the 1st RTT
scheduled
unscheduled
existing flow
new flow
Homa directly sends one BDP of data in 1st RTT
Notes: [c] A second line of work let new flows blindly send traffic in the 1st RTT, such that the one extra RTT can be removed. [c] For example, in Homa, [c] on the arrival of new flows, [c] the sender will send a BDP of unscheduled data packets. [c]

## Slide 13: Current Practice for Handling the One Extra RTT
#1: Pay the cost of one extra RTT
#2: Blindly burst traffic in the 1st RTT
scheduled
unscheduled
existing flow
new flow
buffer overflow
Homa directly sends one BDP of data in 1st RTT
Notes: However, these unscheduled traffic, sent in the first RTT, [c] may cause Large queue build-ups and severe packet loss. As a result, good properties of PCC will be violated. [c]

## Slide 14: Current Practice for Handling the One Extra RTT
#1: Pay the cost of one extra RTT
#2: Blindly burst traffic in the 1st RTT
FCTs of 0-100KB flows with 100Gbps link speed
1000x increase on the tail FCT due to violation of PCC’s properties
tail>25ms
tail<25us
Notes: To demonstrate this problem, [c] we study the flow performance of 0-100 KB small flows under Homa and idealized solution. Flows are generated according to Cache Follower workload. [c] As we can see, compared with idealized solution, the tail FCT under Homa is extremely long. This is because some scheduled packets get lost due to buffer overflows, and trigger flow timeouts. The results indicate that, blind burst can cause serious performance downgrade! [c]

## Slide 15: Can we eliminate 1 RTT extra delay while preserving all the good properties of PCC?
Our answer: Aeolus
Notes: To this end, it is natural to ask such a question: can we eliminate 1 RTT extra delay while preserving all the good properties of PCC? [pause] [click] our answer to this question is Aeolus. [click]

## Slide 16
AEOLUS DESIGN
Notes: Now, we talk about the design of Aeolus. [click]

## Slide 17: Aeolus Overview
Aeolus Control Logic
preserved PCC
for loss recovery
Rate Control
Selective Dropping
Loss Recovery
line-rate start
in the 1st RTT
protect packets
scheduled by PCC
unscheduled packet
scheduled packet
bandwidth
used up
packet
dropped
Notes: This is a design overview. As we can see, Aeolus mainly contains 3 components: rate control, selective dropping and loss recovery.

## Slide 18: Aeolus Overview
Aeolus Control Logic
preserved PCC
for loss recovery
Rate Control
Selective Dropping
Loss Recovery
line-rate start
in the 1st RTT
protect packets
scheduled by PCC
unscheduled packet
scheduled packet
bandwidth
used up
packet
dropped
maximize the chance to utilize spare bandwidth
Notes: Aeolus adopts a minimal rate control at the end hosts: all flows start at line-rate in the first RTT. This can maximize the chance for new flows to utilize spare bandwidth. [c]

## Slide 19: Aeolus Overview
Aeolus Control Logic
preserved PCC
for loss recovery
Rate Control
Selective Dropping
Loss Recovery
line-rate start
in the 1st RTT
protect packets
scheduled by PCC
unscheduled packet
scheduled packet
bandwidth
used up
packet
dropped
preserve all the good properties of PCC
Notes: In the network, to safeguard scheduled packets and preserve all the good properties of PCC, Aeolus introduces a novel selective dropping mechanism at the switch. This mechanism will selectively drop unscheduled packets when spare bandwidth is used up, so scheduled packets will not be affected by unscheduled packets. More details will be introduced later. [c]

## Slide 20: Aeolus Overview
Aeolus Control Logic
preserved PCC
for loss recovery
Rate Control
Selective Dropping
Loss Recovery
line-rate start
in the 1st RTT
protect packets
scheduled by PCC
unscheduled packet
scheduled packet
bandwidth
used up
packet
dropped
fast recovery for dropped unscheduled packets
Notes: Given Aeolus has safeguarded the scheduled packets, loss recovery is needed only for unscheduled packets. In our design, we leverage the well-protected PCC as a safe and efficient means for recovering lost unscheduled packets. [c]

## Slide 21: Selective Dropping Mechanism
2
2
1
1
2
2
Packet tagging at end-host
unscheduled packet (burst in the 1st RTT)
scheduled packet (transmitted by PCC)
Dropping Threshold
Datacenter Fabric
1
2
Egress Queue
Selective dropping in the network
1
Notes: In the next, I will introduce the selective dropping mechanism in details. [c] At the endhost, this mechanism performs packet tagging. [c] Unscheduled and scheduled packets will be tagged with different tags. [c] In the network, switches perform selective dropping to protect Scheduled packets over unscheduled packets. So, what is selective dropping? [c] As we can see, selective dropping is a switch buffer management scheme. [c] It configures a dropping threshold at switch queues. [c] When queue occupancy reaches the preset dropping threshold, [click] the incoming packets carrying low priority tag will get dropped. [click] In contrast, packets carrying high priority tag can still enter the queue. [click]

## Slide 22: Why Selective Dropping Works?
Dropping Threshold
Datacenter Fabric
2
Egress Queue
2
2
2
  Case-1: network is under-utilized
spare bandwidth is utilized & no one extra RTT delay
Notes:   Now, let’s see why selective dropping works. [click] When network is under-utilized, [click] unscheduled packets will enter switch queues. As a result, [click], spare bandwidth is utilized and there is no 1 RTT extra delay. [click]

## Slide 23: Why Selective Dropping Works?
Dropping Threshold
Datacenter Fabric
Egress Queue
2
2
1
  Case-2: network fully-utilized
1
1
2
2
1
2
Low latency & zero loss & fast convergence are preserved for PCC
Notes:   When network is fully-utilized, [click] unscheduled packets are selectively dropped. As a result, [click] scheduled packets are not affected, and [c] all the good properties of PCC are well preserved. [click]

## Slide 24: How to Implement?
  We leverage ECN (Explicit Congestion Notification), a built-in function of commodity switches, for implementation
  What is ECN?
    a switch mechanism which performs congestion notification via marking ECT and CE field in the IP header
ECT | CE | Names for the ECN bits
0 | 0 | Not-ECT (Not ECN Capable Transport)
0 | 1 | ECT(1) (ECN Capable Transport (1))
1 | 0 | ECT(0) (ECN Capable Transport(0))
1 | 1 | CE (Congestion Experienced)
Notes: While the selective dropping mechanism is appealing, the key question is how to implement it with existing commodity switches. [click] We leverage ECN (Explicit Congestion Notification), a built-in function of commodity switches, for the implementation. [c] So What is ECN? [c] ECN is a switch mechanism which allows switch to perform congestion notification via marking a specific field in the IP header.[c] In the IP header, there is a 2-bit field called ECN field. ECN field has 4 codepoints in total. 00 means a flow is not ECN Capable. 01 or 10 means a flow is ECN capable. 11 indicates a flow has encountered congestion in the network. [c]

## Slide 25: ECN-based Implementation
ECN marking threshold
ECN-capable
01
11
ECN marked
  An interesting observation about ECN:
  ECN-capable packets are marked
Notes: In our past testbed experiments with ECN, We made an interesting observation. [click] Let’s assume the queue occupancy reaches the ECN marking threshold. Our finding is that, [click] if a packet is ECN capable, [click] it will enter the queue and get ECN marked. [click]

## Slide 26: ECN-based Implementation
  An interesting observation about ECN:
  ECN-capable packets are marked
  ECN-incapable packets are dropped
ECN marking threshold
ECN-incapable
00
dropped
Notes: [click] But if a packet is not ECN capable, [click] it will be dropped by the switch. [click]

## Slide 27: ECN-based Implementation
  Packet tagging at end-host :
    Scheduled packet tagged as ECN-capable
    Unscheduled packet tagged as ECN-incapable
  ECN configuration at switches:
    ECN marking threshold = selective dropping threshold
Notes:   Based on this observation, we can implement the selective dropping mechanism by reinterpreting the ECN marking function. [click] At the endhost, we tag scheduled packets as ECN-capable, and unscheduled packets as ECN-incapable. [click] At the switch, we set the ECN marking threshold equal to the selective dropping threshold we want to configure. With the above simple configurations, we can implement selective dropping mechanism using existing commodity switches. [click]

## Slide 28: Why not Priority Queueing?
  Priority queueing is an alternative solution
  Scheduled packet  high priority queue
  Unscheduled packet  low priority queue
low priority
high priority
Scheduled packet
Unscheduled packet
Notes:   [click] Priority queueing is an alternative solution to selective dropping mechanism. [click] As shown in the figure, by having scheduled packet enter high priority queue, and unscheduled packets enter low priority, we can also ensure unscheduled packets only utilize the spare bandwidth for the first RTT transfers. [click]

## Slide 29: Why not Priority Queueing?
  Drawback #1: 1 additional queue per service class
  # of supported service classes reduced by half
Notes:   However, priority queueing have two drawbacks. [click] First, it will require one additional queue for each service class, such that the number of supported service classes will be reduced by half. [click]

## Slide 30: Why not Priority Queueing?
  Drawback #1: 1 additional queue per service class
  # of supported service classes reduced by half
  Drawback #2: packet reordering problem
low priority
high priority
6
5
4
2
1
3
6
5
4
2
1
3
6
5
4
2
1
3
Sender
Receiver
Scheduled pkt
Unscheduled pkt
Notes:   Second, due to the queueing delay in the low-priority queue, there can be packet reordering problem. [click] This can be illustrated with a simple example. As shown in the figure, a sender sends 3 unscheduled packets and 3 scheduled packets. [click] in the network, scheduled packets are served with high priority. [click] As a result, scheduled packets with larger sequence number arrive prior to the unscheduled packets, resulting in packet reordering problem. [click]

## Slide 31: Loss Recovery for Unscheduled Packets
  Scheduled packets do not have congestion loss
  Fast Loss detection
    Per packet ACK for each unscheduled packet
    Tail loss probing
      i.e., send a probe right after the transmission of last unscheduled packet
  Fast retransmission
    Reuse preserved PCC to guarantee retransmission
      i.e., retransmit lost packets only with scheduled packets
Notes: With the selective dropping mechanism, scheduled packets are protected from congestion loss. However, unscheduled packets could still suffer from congestion loss under heavy load. To handle this, we designed a fast recovery scheme for unscheduled packets. [click] The first step is to detect loss quickly. [click] To do that, we enable per packet ACK for each unscheduled packet. [c] in Addition, we also design a tail loss probing mechanism for quickly detecting tail loss of unscheduled packets. [c] The second step is to retransmit lost unscheduled packet quickly. [c] Our idea is to reuse preserved PCC to guarantee retransmission. [c] This is done by retransmitting lost packets only with scheduled packets. [c]

## Slide 32: Evaluation Setup
Testbed Setup
  Prototype implementation with DPDK
  8 servers connected to one Mellanox 10Gbps switch
Simulation Setup
  Simulation platforms: NS-2, OMNeT++, htsim
  100Gbps multi-tier spine-leaf DCN topologies
  Realistic production workloads
Notes:   This is the Evaluation setup. [c] For our testbed evaluation, we implement an Aeolus prototype with DPDK. We build a small testbed using 8 servers connected to one Mellanox 10Gbps switch. [c] As for our simulations, we conduct experiments using three simulators including NS-2, OMNeT++ and htsim. We use 100Gbps multi-tier spine-leaf DCN topologies and generate flows according to realistic production workloads.[click]

## Slide 33: Evaluation: ExpressPass + Aeolus
  Aeolus assists ExpressPass to significantly speed up small flows by removing 1 RTT extra delay
60%
80%
30%
Notes:   First, we evaluate whether Aeolus can assist ExpressPass to remove the one RTT extra delay without hurting the good properties of PCC. [c] These three figures show the flow completion times of 0-100KB small flows across three workloads including web server, cache follower and web search. [click] As we can see, with Aeolus, a large portion of small flows complete within the first RTT. [click] This indicates that Aeolus can assist ExpressPass to significantly speed up small flows by removing 1 RTT extra delay. [click]

## Slide 34: Evaluation: Homa + Aeolus
Aeolus can assist Homa to eliminate large queues & loss of scheduled packets, thus significantly improve the tail FCTs.
34
tail>100ms
tail>100ms
tail>30ms
tail<180us
tail<400us
tail<800us
Notes:   Second, we evaluate how Aeolus can assist Homa to preserve the good properties of PCC, without pausing new flows in the first RTT. [c] These three figures show the FCTs of small flows under Homa, with and without Aeolus across three different workloads. [click] As we can see, without Aeolus, flows suffer from very large tail FCT due to packet loss caused by first-rtt burst. [c] But with Aeolus, there is no packet loss and the tail FCT is reduced from > 100ms to be < 800us. [click] This indicates that Aeolus can assist Homa to eliminate large queues & loss of scheduled packets, thus significantly improve the tail FCTs. [c]

## Slide 35: Evaluation: NDP + Aeolus
35
FCT of 0-100KB flows in a two-tier spine-leaf topology
Queue length for the web server workload
Aeolus can assist NDP to achieve similar performance without using expensive customized switches.
Notes:   Third, we evaluate whether Aeolus can assist NDP to achieve similar performance without support from expensive customized switches. [c] The two figures on the left show the FCT of small flows under NDP with and without Aeolus across two workloads. [c] The two figures on the right show the average and the maximum queue length under both schemes using web server workload. As we can see, regarding all the measured metrics, both schemes achieve very similar performance. [c] The results indicate that, Aeolus can assist NDP to achieve similar performance without using expensive customized switches. [c]

## Slide 36: Aeolus Recap
Problem: PCC requires one extra RTT to prepare schedule
Aeolus: a general building block for augmenting PCC schemes
  Line Rate Fast Start  eliminate one RTT extra delay for new flows
  Selective Dropping  preserve all the good properties of PCC
  ECN-based Implementation  compatible with commodity hardware
Notes: Now let me do a brief recap of Aeolus. Aeolus is motivated by the problem that proactive transports requires 1 extra RTT for scheduling packet transmission. To solve this problem, we designed Aeolus, a general building block for augmenting PCC schemes. With Aeolus, three important goals are achieved, including Eliminate one RTT extra delay for new flows, Preserve all the good properties of PCC and Work with commodity switch hardware [click]

## Slide 37
Thanks!
Notes: This is the end of my talk and thank you so much for your attention.